## Slide 1
Chapter 1
Types of Structures & Loads
Saad M Raouf, Ph.D.
Civil Engineering Department
dr.saadraouf@tu.edu.iq
Structural Analysis I

## Slide 2
Structure refers to a system of connected parts used to support load, such as Buildings, Bridges, Towers, Stadiums, ……………. etc.
Introduction

## Slide 3: Topics to Be Addressed
Overview of structures: Definition and examples.
Types of structural elements (e.g., beams, columns, trusses).
Categories of loads (dead loads, live loads, wind loads, etc.).
Structural analysis methods and their applications.
Introduction to structural design considerations.

## Slide 4: Objectives
Introduce the fundamentals of structural analysis and its significance in engineering design.
Understand various types of structures and their components.
Identify different types of loads and their effects on structures.
Develop a systematic approach to analyzing forces and moments in structural elements.

## Slide 5
Structural Analysis involves the prediction of the performance of a given structure under prescribed loads and/or other external effects, such as support movements and temperature changes.
The fundamental purpose of a structural analysis is to determine the magnitudes of force/moment and displacement for each element of a design system for a given set of design loads.
Introduction

## Slide 6
Introduction

## Slide 7
Tie Rods
Structural Elements

## Slide 8: Beams
Type of Beams
Structural Elements

## Slide 9
Columns
Structural Elements

## Slide 10
Trusses
Types of Structures

## Slide 11
Cables
Types of Structures

## Slide 12
Arches
Types of Structures

## Slide 13
Types of Structures

## Slide 14
Frames members are subjected to axial, shear and moment
Frames
Types of Structures

## Slide 15
Surface Structures
Types of Structures

## Slide 16
Types of load:
Loads

## Slide 17
Types of load:
  Dead loads
    Weights of various structural members
    Weights of any objects that are attached to the structure
Loads

## Slide 18
Loads

## Slide 19
Loads

## Slide 20
Loads

## Slide 21
  Live loads
    Varies in magnitude & location
    Building loads
    Depends on the purpose for which the building is designed
    These loadings are generally tabulated in local, or national code
Loads

## Slide 22
  Live loads
    Building Loads
ASCE 7-10 allows a reduction of live load on a member having an influence area (KLL AT) of 400 ft2 (37.2 m2) or more. This reduced live load is calculated using the following equation:
Loads

## Slide 23
Loads

## Slide 24
Loads

## Slide 25
Loads

## Slide 26
    Highway Bridge Loads
    Primary live loads are those due to traffic
    Specifications for truck loadings are reported in AASHTO
Loads

## Slide 27
    Railroad Bridge Loads
    Loadings are specified in American Railroad Engineers Association (AREA)
    A modern train having a 320kN (72k) loading on the driving axle of the engine is designated as an E-72 loading
Loads

## Slide 28
    Impact loads
    Due to moving vehicles
    The % increase of the live loads due to impact is called the impact factor, I
Loads

## Slide 29
    Wind loads
    Effects of wind depends on density & flow of air, angle of incidence, shape & stiffness of the structure & roughness of surface
    For design, wind loadings can be treated as static or dynamic approach
Loads

## Slide 30
    Wind loads
Loads

## Slide 31
Loads

## Slide 32
    Once qz is obtained, the design pressure can be obtained from a list of relevant equations
Loads

## Slide 33
Wind Pressure for Enclosed Building
p  qGCp  qh (GC pi ) (N/m2)
Loads

## Slide 34
Loads

## Slide 35
Loads

## Slide 36
Loads

## Slide 37
Loads

## Slide 38
Loads

## Slide 39
Loads

## Slide 40
Loads

## Slide 41
Design Wind Pressure for Signs F  qhGC p Af
Loads

## Slide 42: Snow Load
If a roof is flat, having a slope of less than 5%, the pressure loading on the roof can be obtained by modifying the ground snow loading pg, by the following empirical formula
pf  0.7Ce Ct Is pg
Loads

## Slide 43
pf  0.7Ce Ct Is pg
Ce = an exposure factor which depends upon the terrain.
Ce = 0.8 for a fully exposed roof in an unobstructed area
Ce = 1.2 for roof located in the center of a large city.
Ct = a thermal factor, refers to the average temperature within the building
Ct = 1.2 for unheated structures kept below freezing,
Ct = 1.0 for normally heated structure.
Is = the importance factor as it relates to occupancy,
Is = 0.80 for agriculture and storage facilities, and
Is = 1.20 for schools and hospitals
Loads

## Slide 44
Loads

## Slide 45: Earthquake Load
    Horizontal accel -> shear forces in the column
    If the column is stiff & the block has a small mass, the period of vibration of the block will be short, the block will acceleration with the same motion as the ground & undergo slight relative displacements
    If the column is very flexible & the block has a large mass, induced motion will cause small accelerations of the block & large relative displacement
Loads

## Slide 46
    Hydrostatic & Soil Pressure
    The pressure developed by these loadings when the structures are used to retain water or soil or granular materials
    E.g. tanks, dams, ships, bulkheads & retaining walls
    Other natural loads
    Effect of blast
    Temperature changes
    Differential settlement of foundation
Loads

## Slide 47
Load combination example:
    Many types of loads can occur simultaneously on a structure (All of them???)
Structural Design

## Slide 48
Where:
D= Dead load.
L = Live load, except roof live load.
Lr = Roof live load.
E = Earthquake load.
W= Load due to wind
F = Load due to fluids
H= Load due to lateral earth pressures
R = Rain load.
S = Snow load.
T = Load due to temperature, shrinkage, creep, differential settlement
Structural Design

## Slide 49
Are you ready?

## Slide 50: Summary
Structures and Loads: Understanding the fundamental relationship between structural components and external forces.
Structural Elements: Key elements like beams, columns, and trusses form the backbone of engineering structures.
Types of Loads: Differentiation between dead loads, live loads, and environmental effects like wind, snow, and earthquakes.
Structural Analysis: Essential methods to predict performance under various load conditions.
Design Implications: The importance of analyzing and combining loads for safe and efficient structural designs.